DESCRIPTION

This work shall consist of furnishing and installing Sign Post, Sign Post Base and Sleeve, as shown on the mcdot standard detail and to the satisfaction of the engineer.  A post shall be placed in the sleeve to prevent accidental tripping on the empty sleeve.

MATERIAL

The post shall be 2” square perforated galvanized tube 12’-0” long.  The post base shall be 2 ¼” square perforated galvanized tube 4’-0” long.  The sleeve shall be 3’-0” x 3 ½” I.D. pipe, galvanized and standard weight.

Concrete shall be Class A concrete, in accordance with NYSDOT Standard Specifications, Section 555, latest revision.

METHOD OF MEASUREMENT

Method of Measurement shall be each sleeve, post base and post installed.

BASIS OF PAYMENT

The unit price bid for each sleeve shall include the cost of pipe, concrete, hardware, and other materials, labor and equipment necessary to complete the job to the satisfaction of the ENGINEER.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C686.07 | Sign Post and Sleeve (12’) | EA |